## Slide 2: Hasta el beacon, todo es bluetooth
Gorka Madariaga
Technical Evangelist, .NET developer
@Gk_8

## Slide 4: Agenda
Beacons
  What’s that?
  Protocols: iBeacon & Eddystone
UWP libraries
  Foreground watcher
  Foreground advertiser
  Working from the background
Community libraries
Xamarin components
Demos – usage examples

## Slide 5: Gorka Madariaga
Proud basketball coach of 14 girls…
…and pseudo-player
Trips to USA organizer (NBA&NFL)
Did I mention that I also do some development?

## Slide 6: Beacons overview

## Slide 7: What is a beacon?
Small ARM computer,
with a Bluetooth Smart connectivity module,
powered by a battery

## Slide 8: What is a beacon?
You can think about the beacon as a small lighthouse
But instead of light, it uses radio waves…and instead of ships, it alerts devices of its presence and info

## Slide 9: Protocols

## Slide 10
Beacons broadcast tiny packets of data, containing their unique ID and information about signal strength and other parameters

## Slide 11: iBeacon
Every iBeacon ID is 20 bytes long and is divided into three sections:
- UUID (16 bytes)
- major number (2 bytes)
- minor number (2 bytes)
Store location |  | New York | Los Angeles | San Francisco
UUID |  | DDD468A7-056B-9E2F-EAE2-6FCE4706331E |  | 
Major |  | 1 | 2 | 3
Minor | Clothing | 10 | 10 | 10
 | Housewares | 20 | 20 | 20
 | Automotive | 30 | 30 | 30

## Slide 12
Proximity beacon advertising package

## Slide 13: Eddystone
Every Eddystone data frame contains the Frame Type information on its first byte:
Frame Type | High-Order 4 bits | Byte Value
UID | 0000 | 0x00
URL | 0001 | 0x10
TLM | 0010 | 0x20
RESERVED | 0011 | 0x30
RESERVED | 0100 | 0x40

## Slide 14: Eddystone-UID
The Eddystone-UID frame broadcasts an opaque, unique 16-byte Beacon ID composed of:
10-byte namespace
6-byte instance
Store location |  | New York | Los Angeles | San Francisco
Namespace |  | DDD468A7-056B-9E2F-EAE2-6FCE4706331E |  | 
Instance | Clothing | 000000000110 | 000000000210 | 000000000310
 | Housewares | 000000000120 | 000000000220 | 000000000320
 | Automotive | 000000000130 | 000000000230 | 000000000330
Notes: The namespace portion of the ID may be used to group a particular set of beacons, while the instance portion of the ID identifies individual devices in the group

## Slide 15: Eddystone-URL
The Eddystone-URL frame broadcasts a URL using a compressed encoding format in order to fit more within the limited advertisement packet
Byte offset | Field | Description
0 | Frame Type | Value = 0x10
1 | TX Power | Calibrated Tx power at 0 m
2 | URL Scheme | Encoded Scheme Prefix
3+ | Encoded URL | Length 0-17

## Slide 16: Eddystone-TLM
Eddystone beacons may transmit data about their own operation to clients
This data is called telemetry and is useful for monitoring the health and operation of a fleet of beacons
Byte offset | Field | Description
0 | Frame Type | Value = 0x20
1 | Version | TLM version, value = 0x00
2-3 | VBATT | Battery voltage, 1 mV/bit
4-5 | TEMP | Beacon temperature
6-9 | ADV_CNT | Advertising PDU count
10-13 | SEC_CNT | Time since power-on or reboot

## Slide 17: UWP libraries Windows.Devices.Bluetooth.Advertisement

## Slide 18: BluetoothLEAdvertisementWatcher watcher
The Bluetooth LE advertisement watcher class is used to control and customize Bluetooth LE scanning
Filter settings available for advertisement data (BluetoothLEAdvertisementFilter) and signal strength (BluetoothSignalStrengthFilter)

## Slide 19: BluetoothLEAdvertisementWatcher watcher
BluetoothLEAdvertisementWatcher watcher =
new BluetoothLEAdvertisementWatcher { ScanningMode = BluetoothLEScanningMode.Active };
watcher.Received += WatcherOnReceived;
watcher.Start();
[…]
void WatcherOnReceived(BluetoothLEAdvertisementWatcher sender, BluetoothLEAdvertisementReceivedEventArgs eventArgs)
{
// Do stuff with received data
}

## Slide 20: BluetoothLEAdvertisementPublisher publisher
The Bluetooth LE advertisement publisher class is used to control and customize Bluetooth LE advertising
Your device can turn to a virtual beacon broadcasting the data frames you set on a BluetoothLEManufacturerData instance to be advertised by the publisher

## Slide 21: BluetoothLEAdvertisementPublisher publisher
var writer = new DataWriter();
UInt16 uuidData = 0x1234;
writer.WriteUInt16(uuidData);
var manufacturerData = new BluetoothLEManufacturerData();
manufacturerData.CompanyId = 0x0006;
manufacturerData.Data = writer.DetachBuffer();
BluetoothLEAdvertisementPublisher publisher =
new BluetoothLEAdvertisementPublisher();
publisher.Advertisement.ManufacturerData.Add(manufacturerData);
publisher.Start();

## Slide 22: Background tasks
For background usage, there are triggers available for both scanning (BluetoothLEAdvertisementWatcherTrigger) and publishing (BluetoothLEAdvertisementPublisherTrigger)
Both have the same structure their foreground peers have, so you can set filters for scanning and data to be broadcasted for publishing

## Slide 23: [COMMUNITY] Universal Beacon Library
Provides an easy way for Universal Windows Apps to manage beacons and parse their information packages
Directly use the received Bluetooth Smart Advertisement notifications from the Windows 10 base system
It extracts, combines and updates unique beacons, associated individual frames to the beacons, and parses their contents
https://github.com/andijakl/universal-beacon

## Slide 24: Demo time Raw and parsed payloads

## Slide 25: Ranging beacons

## Slide 26: RSSI and TxPower
RSSI is the received signal strength indicator (in dBm)
Strongest as the beacon is closer
TxPower (aka Measured Power) is the average RSSI received at 1 meter distance (in dBm)

## Slide 27: Formula
double ratio = Rssi * 1.0 / txPower;
if (ratio < 1.0)
Distance = Math.Pow(ratio, 10);
else
Distance = (0.89976) * Math.Pow(ratio, 7.7095) + 0.111;

## Slide 28: Proximity range
Thanks to the distance calculation, using RSSI and TxPower, we can know how close our device is from any beacon

## Slide 29: Demo time Beacon radar

## Slide 30: Demo time And it includes toast notifications!
X
You missed me?

## Slide 31: Connecting to the cloud

## Slide 32: Demo project overview
UWP app
Dashboards and Visualizations
Power BI
Business Scenarios
Recommendations,
customer churn,
forecasting, etc.
Azure
Stream Analytics
Azure
Event Hub
People
Automated Systems
Xamarin app
Azure SB Lite
Com.Xamtastic.Patterns.Azure.EventHub

## Slide 33: No Event Hub support for UWP? No problem
[COMMUNITY] Azure SB Lite .
Access to Microsoft Azure Service Bus from different platforms using AMQP protocol
https://github.com/ppatierno/azuresblite

## Slide 34: Demo time Connecting to the cloud

## Slide 35: Bonus track: Xamarin components

## Slide 36: Estimote SDK
public void ScanForBeacons ()
{
BeaconManager beaconManager;
BeaconRegion region;
beaconManager = new BeaconManager ();
beaconManager.ReturnAllRangedBeaconsAtOnce = true;
var uuid = new NSUuid (“Common-UUID-to-monitor");
region = new BeaconRegion (uuid, "BeaconSample");
beaconManager.StartRangingBeaconsInRegion(region);
beaconManager.RangedBeacons += (sender, e) => {
new UIAlertView("Beacons Found", "Just found: "
+ e.Beacons.Length + " beacons.",
null, "OK").Show();
};
}
Component ready to use
https://components.xamarin.com/gettingstarted/estimotesdkios

## Slide 37: [COMMUNITY] Com.Xamtastic.Patterns.Azure.EventHub
Another community library to help us sending messages to Azure EventHub using HTTP protocol
https://www.nuget.org/packages/Com.Xamtastic.Patterns.Azure.EventHub/
[!!] Requires SharedAccessSignature generation

## Slide 38: Demo time Take a look at the Xamarin code

## Slide 39: Wrapping up…

## Slide 40: Lessons learned
NSLocationAlwaysUsageDescription and/or
NSLocationWhenInUseUsageDescription really can ruin your weekend…
Cloud is always on the picture
Don’t re-invent the wheel!

## Slide 41: Nothing but <3 for .NET Community

## Slide 43: Useful links…
UWP Bluetooth advertising sample
https://github.com/Microsoft/Windows-universal-samples/tree/master/Samples/BluetoothAdvertisement
Company identifiers
https://www.bluetooth.com/specifications/assigned-numbers/company-Identifiers
Eddystone protocol reference
https://github.com/google/eddystone
iBeacon protocol reference
https:// developer.apple.com/ibeacon/Getting-Started-with-iBeacon.pdf

## Slide 44: …and demo code is already uploaded
http://github.com/gk-8/beacon-insights
keep in mind it’s for demo purposes 

## Slide 45
http://aka.ms/DOTNETT3S4

## Slide 46
Gorka Madariaga
Technical Evangelist, .NET developer
@Gk_8
http://aka.ms/DOTNETT3S4